## Slide 1: The Internet of Attack Vectors Exploration and Remediation of Vulnerabilities in Non-Computing Consumer Wireless Devices Richard Givens CPSC 59700, Section 4, Research in Computer Science Lewis University, College of Arts and Science Spring, 2017

## Slide 2: Who Am I?
Former Law Enforcement Officer with over seven years of investigative experience
Prior Service, US Marines, currently enrolled in the Department of Veterans Affairs Vocational Rehabilitation Program
Bachelors of Science in Computer Information Systems
Bachelors of Science in Management Information Systems
Graduate Student of Computer Science at Lewis University
Independent Computer and Information Systems Consultant
Member at large of the Chicago area InfoSec Community
Product Manager for an AMD Graphics Partner Company
Richard “Rick” Givens

## Slide 3: What Is The Purpose of This Project?
Provide an overview of the vulnerabilities affecting IoT Devices
Provide a demonstration of these vulnerabilities with a commercial device that has no previously disclosed issues (Original work!)
Provide a general synopsis of methods used to exploit these vulnerabilities
Disclose the discovered security flaws, giving the distributor time to address them
Provide an overview of effective remediation and patching

## Slide 4: The Testing Platform
IoT Device – Black + Decker Wi-Fi Enabled 6-Quart Slow Cooker
  Connects to a network
  Controllable via companion app available for iOS and Android
Huawei (pronunciation: Wah Way) Honor 6X Android Smartphone
Lenovo Yoga Laptop
  Intel Core i5 6th Generation | 16 Gigabytes of DDR 3 1600 Low Voltage RAM
  Kali Linux (USB Persistent Mode)
Custom Desktop PC
  AMD Ryzen 7 1700X Watercooled CPU | 32 Gigabytes of DDR4 3000 RAM
  Windows 10 64 bit hosting a Kali Linux Virtual Machine

## Slide 5: Legal Disclaimer – Danger Hacking Ahead!
All testing, implementation and research was conducted on, and with, personally owned equipment
All tools utilized are open source
Specific methodologies which could serve as a blueprint will not be discussed
There was no modification of source code or hardware
Richard Givens 2016

## Slide 6: Key Terms
Botnet
DoS | DDoS | DoC
Evil Twin
Hacker
IoT
Kali Linux
Man in the Middle
nmap
Wireshark
Spy vs Spy, MAD Magazine, Source Image: Clipartfest.com

## Slide 7: The Internet of Things is everywhere it shouldn’t be.
In 2017, an estimated 20 billion IoT devices were installed worldwide.
By 2019, the global market for IoT devices is estimated to reach almost two trillion U.S. Dollars.
Examples of IoT devices include smart refrigerators, smart TVs, Wi-fi connected appliances and NEST Thermostats.
Any consumer device capable of sending or receiving network signals is part of the Internet of Things.
Image Courtesy of INTERSOG Group, iot.intersog.com

## Slide 8: IoT Devices Are Convenient
Smart appliances are controllable from a distance
Provide status reporting
Combine features of multiple devices in a single device
Increase efficiency and provide cost savings
Affordable by many, no longer a status symbol for the wealthy
Tam Hulusi “ CES 2016 and IoT: Observations on Security and Convenience”, Source: LinkedIn

## Slide 9: IoT Devices Are Neat
Conversation starters
Status symbol
Plays to our natural fascination with technology
As more devices are connected to the IoT, we become increasingly convinced we need them.
Image courtesy of Internet of More Things, IOMT Newsletter

## Slide 10: IoT Devices are Vulnerable
2000
2016
Dyn Corporation
2017
Private University
Kapersky
Internet connected
devices will become a
target for criminals
Mirai botnet uses
routers and DVRs to
disrupt DNS services
(un-named)
56 Hour DDoS using CCTV Cameras
Image courtesy of The Hacker News, September 27, 2016

## Slide 11: Examination of the Black + Decker Wi-Fi Enabled 6-QT Slow Cooker
Scw3000s
Country of Manufacture: China
Original Model Name: Midea Group TC6006w
802.11g/b/n Wireless Network Compatible
Operates on the 2.4GHz band across 11 channels up to 135Mbps
Product Image courtesy of Black + Decker

## Slide 12: What Did I Find?
Hardcoded administrative password in firmware
Hardcoded broadcast SSID
Accepts connections from any device using the SSID and password
Accepts multiple concurrent connections
Weak password policy in smartphone app
Account creation prompts automatic sending of notification email to the user
No account verification or authentication required
Accepts arbitrary input during account registration

## Slide 13: What Were The Methods?
Smartphone App – Manual entry and observation of results
Device Connections – Searching broadcast SSID and password entry
Evil Twin – Kali Linux built in tools: nmap, airbase-ng
Man in the Middle – Kali Linux built in tools: Wireshark

## Slide 14: What Are The Implications?
Hardcoded passwords provide avenue of attack allowing infection by malware, as well as access to and modification of firmware
Hardcoded SSID provides easy method of duplication as well as allowing easier access for malware and attacks as above
Any number of devices may connect concurrently, all they need is the SSID and password
Users are vulnerable to both Evil Twin and Man in the Middle Attacks exposing both the connecting smartphone and the connected network to exploitation (not uncommon)
Multiple fake user accounts may be created, using a botnet or a click farm, this will result in overwhelming the notification email server, eventually causing deadlock

## Slide 15: Formal Disclosure
Standard procedure for information security professionals researching and discovering vulnerabilities.
Consulted with established professionals to confirm findings.
Contacted Black + Decker via phone on May 12, 2017, sent to voicemail.
Emailed Black + Decker Support Team on May 13, 2017.
No response received, public disclosure will proceed after May 19, 2017.
Image Courtesy of Sobering Thoughts

## Slide 16: Remediation and Solutions
Immediately cease automatic email notification of every new account creation
Scan the user database for obvious fake entries
Deletion of obvious fake accounts discovered in the scan
Develop a working plan in tandem with the developer, Midea Group, to address hardware and software vulnerabilities
Beaker, The Muppet Show, Source Image: Pinterest

## Slide 17: Patching and Protecting Against Future Exploitation
Unlikely to occur
The original developer may be unwilling, uncooperative or indifferent
Requires overhaul of the companion App
Requires overhaul of the slow cooker’s firmware
Implements strong password policy
Addresses number of users per device
Addresses number of concurrent connections to any single device
Prevents arbitrary input by allowing only top level domains
Prevents fake accounts by requiring email authentication and verification
Allows users to change SSID and passwords
Richard Givens 2017

## Slide 18: Conclusion
IoT devices developed without robust testing methods present serious risks to consumers and businesses
As the amount of globally installed IoT devices grows, the security and privacy risks increase proportionately
Third party resellers, distributors and companies which engage in rebranding do not understand the full range of risks, and are ill equipped to address them
It is reasonable to assume that any IoT device suffers from one or more of the commonly disclosed IoT vulnerabilities
Poor software implementation may create unexpected vulnerabilities which will eventually result in negative consequences for the companies in question
Users and consumers must be proactive, taking their personal data and information security in their own hands
Do not trust, always verify

## Slide 19: Ongoing Research
Continue to explore the slow cooker for other vulnerabilities, and disclose them, if found
Duplicate attacks in a research setting to become familiar with the methodology and tools of malicious hackers
Specifically, attempt to gain access to the slow cooker’s filesystem
Attempt to develop a patch or patches for discovered security flaws
Develop a comprehensive methodology for testing IoT devices and remediating security flaws

## Slide 20: Links and References (Informal List)
“FCC Documentation.” FCC Documentation, apps.fcc.gov/eas/GetApplicationAttachment.html?id=3115790.
“FCC ID TAPMD-TC6006W Slow Cooker by Guangdong MD Consumer Electric Manufacturing Co., Ltd.” FCCID.io, fccid.io/TAPMD-TC6006W. Accessed 13 May 2017.
“Global Internet of Things Market Size 2009-2019 | Statistic.” Statista, www.statista.com/statistics/485136/global-internet-of-things-market-size/. Accessed 13 May 2017.
Hanlon, Mike. “LG Internet Refridgerator.” New Atlas - New Technology & Science News, New Atlas, 4 June 2004, newatlas.com/go/1132/. Accessed 13 May 2017.
Harrison, Linda. “Fridges to Be Hit by Net Viruses.” • The Register, 21 June 2000, www.theregister.co.uk/2000/06/21/fridges_to_be_hit_by/. Accessed 13 May 2017.
Harvey, Brian. “What Is a Hacker.” What Is a Hacker?, Universit of Berekley, California, people.eecs.berkeley.edu/~bh/hacker.html. Accessed 13 May 2017.
“Internet of Things (IoT) History.” History of IoT | Background Information and Timeline of the Trending Topic, www.postscapes.com/internet-of-things-history/. Accessed 13 May 2017.
“IoT Devices Installed Base Worldwide 2015-2025 | Statistic.” Statista, www.statista.com/statistics/471264/iot-number-of-connected-devices-worldwide/. Accessed 13 May 2017.
“Krebs on Security.” Brian Krebs, krebsonsecurity.com/tag/mirai-botnet/. Accessed 13 May 2017.
“LG Electronics Introduces Digital Refrigerator.” Appliance Design Magazine RSS, www.appliancedesign.com/articles/89516-lg-electronics-introduces-digital-refrigerator. Accessed 13 May 2017.
“Nmap.” Nmap: the Network Mapper - Free Security Scanner, nmap.org/. Accessed 13 May 2017.
“Norton - Antivirus Software and Spyware Removal.” Norton - Antivirus Software and Spyware Removal, us.norton.com/botnet/. Accessed 13 May 2017.
“Our Most Advanced Penetration Testing Distribution, Ever.” Kali Linux, Offensive Security, www.kali.org/. Accessed 13 May 2017.
“WiFi-Enabled 6-Quart Slow Cooker.” WiFi-Enabled 6-Quart Slow Cooker | BLACK + DECKER, Black + Decker, www.blackanddeckerappliances.com/products/cooking-appliances/slow-cookers/SCW3000S-Wifi-Enabled-6-Quart-Slow-Cooker-Silver.aspx. Accessed 13 May 2017.
“Wireshark · Go Deep.” Wireshark · Go Deep., www.wireshark.org/. Accessed 13 May 2017.